## Slide 1: An Energy-efficient Multi-core Restricted Boltzmann Machine Processor with On-chip Bio-plausible Learning and Reconfigurable Sparsity
1Jiajun Wu, 1Xuan Huang, 1Le Yang, 1Liang Wang, 1Jipeng Wang, 3Zuozhu Liu, 4Kwen-Siong Chong, 2Shaowei Lin and 1Chao Wang
1. Huazhong University of Science and Technology, Wuhan, China
2. Singapore University of Technology and Design, Singapore
3. National University of Singapore, Singapore
4. Nanyang Technological University, Singapore

## Slide 2: Outline
Background
Previous RBM Processor
VPF Learning Rule
Proposed RBM Processor
Measurement Results and Comparison
Conclusions and Future Work

## Slide 3: Background (1/2)

## Slide 4: Background (2/2)
Original image
Reconstructed image
Hidden Layer
Visible Layer
Restricted Boltzmann Machine (RBM) Model
Traditional learning rule - Contrastive Divergence (CD)
Unsupervised learning – No labels required.
Less computation complexity compared with Deep Neural Networks
1
0
1
1
1
0

## Slide 5: Previous RBM Processor (1/2)
Large external storage
High bandwidth required
DDR
FPGA
On-Chip
Need extra devices (FPGA, DDR memory) for data communication
[3] C. Tsai et al., “A 41.3pJ/26.7pJ per neuron weight RBM processor for on-chip learning/inference applications,” Proc. IEEE A-SSCC, pp. 265-268, Nov. 2016.

## Slide 6: Previous RBM Processor (2/2)
NoC based Spiking RBM processor
Spiking CD, semi-supervised learning
[4] G. K. Chen et al., “A 4096-neuron 1M-synapse 3.8-pJ/SOP spiking neural network with on-chip STDP learning and sparse weights in 10-nm FinFET CMOS,” IEEE JSSC, vol. 54, no. 4, pp. 992-1002, Apr. 2019.
LUT based weight update strategy
Semi-supervised learning still needs label information.
Large area consumption for weight update LUT.
Low flexibility due to spikes based architecture.

## Slide 7
VPF Learning Rule
Advanced learning rule - Variational Probability Flow (VPF)
Bio-plausible and unsupervised learning rule.
Only one generation phase (phase 2) which needs Gibbs Sampling (GS).
[5] Z. Liu et al., “Variational probability flow for biologically plausible training of deep neural networks,” Proc. AAAI 2018.
STDP

## Slide 8: Proposed RBM Processor (1/7)

## Slide 9: Proposed RBM Processor (2/7)
M × M RBM model is mapped into a mesh of n × n RBM cores.
Asynchronous accumulation of different partial summations.
Sparse connection in RBM core.

## Slide 10: Non-linearity of pull-down DR
I-V characteristic of pull-down driver
Pull-down driver

## Slide 11: Effect of non-linearity of pull-down DR
Conventional driver
Proposed driver
RT = 50 Ohm, TX pin C = 1.7pF L=2.5nH, RX pin C = 1.7pF L=2.5nH
No appreciable difference between proposed and conventional drivers

## Slide 12: All-synthesizable 2-tap FFE
6Gbps FF not used for 1T delay, because it cannot be implemented by synthesis

## Slide 13: DLL for 1T delay generation
For DLL operation, training patterns are used (1010…)
1T = (delay of coarse delay line + delay of fine delay line)

## Slide 14: Proposed 2-tap FFE driver with 2-to-1 serializer

## Slide 15: Final proposed all-synthesizable voltage-mode TX

## Slide 16: Chip photo and layout

## Slide 17: Measurement setup

## Slide 18: Measured eye-diagram (6Gbps)

## Slide 19: Performance summary

## Slide 20: Conclusion
6Gbps voltage-mode TX synthesized with 2-tap FFE
Wide eye-opening achieved @ 1.4m FR4 channel
1-bit-period delay generation circuit for FFE because 6Gbps F/F cannot be implemented by synthesis